A utilização da eletromiografia na Saúde do Trabalhador

OLIVEIRA, Giane S1

CEZAR-VAZ, Marta R2

ROCHA, Laurelize P3

SEVERO, Luana O4

LIMA, Liliana M 5

SILVA, Daiane F6

Resumo:

PALAVRAS CHAVE: Eletromiografia. Saúde do trabalhador.

INTRODUÇAO: Diante da elevada taxa de acorrência dos distúrbios osteomusculares é necessário que os profissionais de saúde adotem métodos que promovam a identificação destas afecções, tais como a eletromiografia. Objetivo: Identificar a finalidade dos estudos quanto à utilização da eletromiografia na área da saúde do trabalhador. Metodologia: Trata-se de uma revisão integrativa, na seleção foi utilizada a associação dos descritores “eletromiografia” e “saúde do trabalhador” nas bases de dados MEDLINE e CINAHL. Obedecendo aos critérios de inclusão: artigos científicos, disponíveis na íntegra, publicados nos idiomas português, inglês ou espanhol, até 2010. Resultados: Foram selecionados 19 artigos. Os estudos apresentaram como finalidade: desenvolver um sistema de apoio informatizado para a construção residencial, investigar o movimento da coluna vertebral, esforço muscular durante o trabalho, identificar o nível de fadiga durante atividades laborais, reduzir o desconforto muscular na região lombar, prever os padrões de atividade no trabalho de limpeza, quantificar a variabilidade do tronco, coluna vertebral em movimentos de elevação e identificar os fatores do ambiente de trabalho que influenciam a variabilidade biomecânica, investigar a eficácia de um instrumento para pegar objetos em uma linha de montagem automotiva. Conclusão: Os estudos buscam identificação dos padrões de atividade muscular durante o trabalho, assim como medidas para a melhoria de suas condições laborais.

REFERENCIAS:

1.Boden, A; Oberg, K. Torque resistance of the passive tissues of the trunk at axial rotation. Applied Ergonomics, Vol 29, No.2,  1998,  111-118.

2.Caboor, D. E. et al. Implications of an adjustable bed height during standard

nursing tasks on spinal motion, perceived exertion and muscular activity. ERGONOMICS, 2000, VOL. 43, NO. 10, 1771 - 1780.

3.Chan, RFM et al. Self-perceived exertion level and objective evaluation of neuromuscular fatigue in a training session of orchestral violin players. Applied Ergonomics, Vol. 31, 2000, 335 -341.

4.Granata, KP et al. Variation in spinal load and trunk dynamics during repeated lifting exertions. Clinical Biomechanics, Vol. 14,1999,  367 - 375.

5.Graham, RB et al. Effectiveness of an on-body lifting aid at reducing low back physical demands during an automotive assembly task: Assessment of EMG response and user acceptability. Applied Ergonomics, Vol. 40, 2009;  936–942.

6.Hagg, GM et al. Forearm muscular load and wrist angle among automobile assembly line workers in relation to symptoms. Applied Ergonomics, Vol. 28, No 1, 1997; 41 - 47.

7.Hermans,V et al. Lipoatrophia semicircularis and the relation with office work. Applied Ergonomics, Vol. 30, 1999,  319 - 324.

8.Holtermann, A. et al. The influence of biofeedback training on trapezius activity and rest during occupational computer work: a randomized controlled trial. Eur J Appl Physiol (2008) 104:983–989.

9.IWAKIRI, K et al. Shape and Thickness of Cushion in a Standing Aid to Support a Forward Bending Posture: Effects on Posture, Muscle Activities and Subjective Discomfort. Industrial Health, Vol. 42, 2004, 15–23.

10.IWAKIRI, K et al. Effects of a Standing Aid on Loads on Low Back and Legs during Dishwashing. Industrial Health, Vol. 40,  2002, 198–206.

11.Laursen, B et al. Biomechanical model predicting electromyographic activity in three shoulder muscles from 3D kinematics and external forces during cleaning work. Clinical Biomechanics, Vol. 18, 2003; 287–295.

12.Meyer,RG; Radwin, RG. Comparison of stoop versus prone postures for a simulated agricultural harvesting task. Applied Ergonomics, Vol. 38 , 2007, 549–555.

13.Mirka, G A. et al. An evaluation of arborist handsaws. Applied Ergonomics 40 (2009) 8–14.

14.Nussbaum, MA. et al.Development of a decision support system for residential construction using panellised walls: Approach and preliminary results. Ergonomics, Vol. 52, No. 1, January 2009, 87–103.

15.Nussbaum, MA et al. Fatigue and Endurance Limits During Intermittent Overhead Work. AIHAJ, v62, no4; 2001, p446-56.

16.Poosanthanasarn, N. et al. REDUCTION OF LOW BACK MUSCULAR DISCOMFORT THROUGH AN APPLIED ERGONOMICS INTERVENTION PROGRAM. J TROP MED PUBLIC HEALTH, Vol 36 nº 4. 2005.

17.Shergill et al. Pinch force and forearm-muscle load during routine colonoscopy:a pilot study. GASTROINTESTINAL ENDOSCOPY Volume 69, No. 1; 2009.

18.UDO, H et al. The Effect of a Tilting Seat on Back, Lower Back and

Legs during Sitting Work. Industrial Health , Vol.37, 1999,  369-381.

19.Wahlstrom,J et. al. Perceived muscular tension, emotional stress, psychological demands and physical load during VDU work. Int Arch Occup Environ Health, Vol. 76, 2003: 584–590.